## Slide 1
Low Cost Real-time Room
Occupancy Indicating System
Chirag Shah, Srijal Poojari Guide: Prof. Priya Deshpande
Department of Electronics Engineering, Sardar Patel Institute of Technology, Andheri (West), Mumbai-400058
Introduction
The objective of this project was to tackle a problem faced by corporate environments.
In a typical corporate environment there exists multiple conference/meeting rooms.
Anyone can book any meeting room for any time (if the room is available) using a mobile app
Solution Design
Conclusions
References
[1] Sparkfun.com, “nRF24L01+ Transceiver Hookup Guide”, [Online]. Available:https://learn.sparkfun.com/tutorials/nrf24l01-transceiver-hookup-guide [Accessed: 10-Feb-2018]
[2] geekstips.com, “Internet of Things Project – Communication between ESP8266 modules”, [Online]. Available: https://www.geekstips.com/two-esp8266-communication-talk-each-other/ [Accessed: 10-Feb-2018]
[3] Scargill, “Networking the nef24l01”, [Online]. Available:https://scargill.wordpress.com/2013/05/17/networking-the-nrf24l01/ [Accessed: 10-Feb-2018]
Future scope includes reducing the power consumption of nodes by utilizing microcontroller sleep techniques.
We may have an opportunity to implement this in a real life corporate environment
Problem Definition
Employees require frequent access to these meeting rooms, but lack of real-time knowledge of its availability leads to inconvenient hassle.
The problem was that anyone could book a meeting room and then not use it. Or if someone wanted to have a meeting without pre-booking the meeting room the he/she would have to go from room to room to check the availability of the rooms. The would create a lot of unnecessary hassle and would lead to unoptitmal utilization of the workspace.
We used a PIR sensor to detect occupancy of the room
The sensor is connected to an Atmel microcontroller which relays the information to a central device via radio modules configured in a mesh configuration
The central device will push the data to the internet using an RF module.
All the devices are battery powered
Since the devices are battery powered – we used a low dropout voltage, low quiescent current voltage regulator. This improved the quiescent current to 17uA compared to 5mA used by a standard voltage regulator like a LM1117. Also the dropout voltage improved to 100mV from a typical 1.5v.
Results
Highlights
We created a complete end-to-end product
Designed a network of wireless battery operated devices with PCBs professionally manufactured
3D printed the product housing
Designed the web interface
Work Done
Designed the prototype of the circuit on breadboards which included the microcontroller, radio module and an OLED display
Designed the PCB of the circuit in Eagle and got it manufactured from a PCB prototyping service (PCBway.com)
We assembled the board
We manufactured the housing unit using 3D printing
The end product
Web interface showing the occupancy status each room
Web interface to show the occupancy status of each room
Inside the housing of the final product